Companion Website
Commands are referenced on our companion website – for easy copy & paste!
Section Name HERE!
https://training.ny-central.com/bhyve101

---
Preparing Your System
Create a /lab directory
UFS
mkdir /lab
ZFS
zfs create <zpool>/lab
Downloads

---
Preparing Your System
Download required files while we talk about the basics!
Downloads

---
bhyve is...
Hypervisor – Type I vs II
Guest
Downloads
Guest
Hypervisor
Hypervisor
OS

---
bhyve is not...
Downloads
rc.d

---
Basics of a VM
CPU
Memory
Host Bus / Bridge
Downloads
Disk & Controller
Firmware
Network

---
System Requirements
CPU w/ virtualization support
Virtualization enabled in BIOS
Firmware packages installed
edk2-bhyve
bhyve-firmware
Relevant kernel modules loaded
Package Setup

---
Kernel Modules
These Kernel Modules must be loaded
vmm for virtualization
nmdm for use of serial console
tap for use of virtual network interface
Put into loader.conf:
vmm_load=”YES”
nmdm_load=”YES”
tap_load=”YES”
Environment Setup

---
Kernel Module Loading
if ! kldstat -q -m vmm; then
   if kldstat -q -n vmm; then
      bail 1 "Error: VMM loaded but
      not active. Is VMX disabled via
      BIOS?"
   fi
   bail 1 "Error: VMM not loaded
        (pci/ppt not active)."
fi
Environment Setup

---
The bhyve commands
bhyve
user space daemon
bhyveload
Load a FreeBSD kernel into a virtual machine
bhyvectl
Create and destroy a virtual machine
Downloads

---
The bhyve components
bhyve user space daemon
/dev/vmm
Downloads
vmm kernel module

---
If everything else fails...
Read the manual!
man bhyve
man bhyveload
man bhyvectl
man vmm
Downloads

---
VM life cycle
bhyvectl or bhyveload – create guest
bhyve – runs guest
Downloads
bhyvectl – destroys guest

---
Initiating a VM
bhyvectl --create --vm=<vmname>
Creates an “empty” guest and readies it for loading a guest OS/machine into it.
Once completed, we run bhyve.
bhyve -D ensures destruction after use.
bhyvectl --destroy --vm=<vmname>
Downloads

---
Basics of a VM
CPU
Memory
Firmware
Downloads
Host Bus / Bridge
Disk & Controller
Connectivity

---
Defining the VM
CPU
numcpu – number of CPUs
socket – number of sockets
core – number of cores
-c <numcpu>:<socket>:<core>
-c <numcpu>
-c 4
Downloads

---
Basics of a VM
CPU
Memory
Firmware
Downloads
Host Bus / Bridge
Disk & Controller
Connectivity

---
Defining the VM
Memory
Can be specified with unit
M, G, m, g
-m 2G
Downloads

---
Basics of a VM
CPU
Memory
Firmware
Downloads
Host Bus / Bridge
Disk & Controller
Connectivity

---
Defining the VM
UEFI Firmware
Required for graphical console and VNC
Works with or without variables file
defined as device behind LPC PCI-ISA bridge
requires lpc PCI-ISA bridge
-l bootrom,/usr/local/share/uefi-firmware/BHYVE_UEFI_CODE.fd
Downloads

---
Defining the VM
UEFI Firmware – Using a variables file
cp /usr/local/share/uefi-firmware/BHYVE_UEFI_VARS.fd \
/root/vars.fd
-l bootrom,/usr/local/share/uefi-firmware/BHYVE_UEFI_CODE.fd,
/root/vars.fd
Downloads

---
Basics of a VM
CPU
Memory
Firmware
Downloads
Host Bus / Bridge
Disk & Controller
Connectivity

---
Defining the VM
PCI bus component
Host Bridge (Generic or AMD)
LPC PCI-ISA bridge
Pass-Through PCI
Network Device
Storage Device
Frame Buffer Device (Console)
Serial Console
Audio Controller
Downloads

---
Defining the VM
PCI bus component addressing
pcislot
pcislot:function
bus:pcislot:function
Ranges
bus 0-255
pcislot 0-31
function 0-7
Downloads

---
Defining the VM
PCI bus component
-s <pciaddress>,<component>
Some components offer additional parameters, each added with a comma (,)
Downloads

---
Defining the VM
Hostbridge component
hostbridge
hostbridge_amd
Caveats
Usually in slot 0
Required by most Operating Systems
-s 0,hostbridge
Downloads

---
Defining the VM
LPC PCI-ISA bridge
lpc
-s 1,lpc
Downloads

---
Basics of a VM
CPU
Memory
Firmware
Downloads
Host Bus / Bridge
Disk & Controller
Connectivity

---
Defining the VM
Storage component – multiple backends
ahci – SATA Disk
ahci-cd – SATA CD-ROM
virtio-blk – Virtual Block I/O
nvme
Best performance: usually nvme
-s 10,nvme,/pathtodisk.img
-s 11,ahci-cd,/pathto.iso
Downloads

---
Preparing a Disk Image
Creating a sparse disk image
UFS:
truncate -s <size> /pathto.img
ZFS - like UFS or:
zfs create -V <size> <zpool/path/img>
creates device node at
/dev/zvol/zpool/path/img
Disk Setup

---
What we have so far
bhyve -c 4 -m 2G \
-l bootrom,/usr/local/share/uefi-firmware/BHYVE_UEFI_CODE.fd,
/lab/freebsd-vm/vars.fd \
        -s 2,ahci-cd,/lab/freebsd.iso \
        -s 3,nvme,/lab/freebsd-vm/disk.img \
        -s 1,lpc \
        freebsd-vm
Downloads

---
Basics of a VM
CPU
Memory
Firmware
Downloads
Host Bus / Bridge
Disk & Controller
Connectivity

---
Virtual Serial Cable
B
/dev/nmdm0
A
Downloads

---
Defining the VM
Serial Console
lpc – required
-l,com<comport> – goes 1 – 4
Relevant arguments:
-l com1,/dev/nmdm0B \
-s 1,lpc
Downloads

---
What we have so far
bhyve -c 4 -m 2G \
-l bootrom,/usr/local/share/uefi-firmware/BHYVE_UEFI_CODE.fd,
/lab/freebsd-vm/vars.fd \
-l com1,/dev/nmdm0B \
        -s 2,ahci-cd,/lab/freebsd.iso \
        -s 3,nvme,/lab/freebsd-vm/disk.img \
        -s 1,lpc \
        freebsd-vm
Downloads

---
Virtual Serial Cable
B
/dev/nmdmfreebsd-vm0
A
Downloads

---
What we have so far
bhyve -c 4 -m 2G \
-l bootrom,/usr/local/share/uefi-firmware/BHYVE_UEFI_CODE.fd,
/lab/freebsd-vm/vars.fd \
-l com1,/dev/nmdmfreebsd-vm0B \
        -s 2,ahci-cd,/lab/freebsd.iso \
        -s 3,nvme,/lab/freebsd-vm/disk.img \
        -s 1,lpc \
        freebsd-vm
1st Boot

---
Serial Console Config
Add to guest’s loader.conf for switch to serial console after boot:
console=”comconsole”
Otherwise, some boot messages and issues may be missing on serial output (i.e. fsck)!
Guest Config

---
Shutdown & Reboot
Gracefully
On host: kill -TERM <bhyvepid>
On guest: poweroff, shutdown, …
Forcing from host:
bhyvectl --destroy –vm=<vmname>
Reboot only through destroying and restarting bhyve process on host.
Attach a Network Device

---
Exit Codes
bhyve tells you what caused process exit
0 – reboot (please)
1 – powered off
2 – halted
3 – triple fault
4 – error
Attach a Network Device

---
Using tmux instead
tmux new-session -d -s bhyve 'bhyve \
        -H \
        -c 2 \
        -D \
        -l com1,stdio \
        -l bootrom,/usr/local/share/uefi-firmware/BHYVE_UEFI.fd \
        -m 2G \
        -s 0,hostbridge \
        -s 1,ahci-cd,/lab/freebsd.iso \
        -s 2,nvme,/lab/freebsd-vm/disk.img \
        -s 3,lpc \
        freebsd-vm'
1st Boot

---
Defining the VM
framebuffer component
tcp – IP address and port
w – screen width
h – screen height
password
wait – wait for connection, then boot
xhci,tablet component for mouse input
-s 4,fbuf,tcp=127.0.0.1:5900,w=1600,h=900,password=secret,wait \
        -s 5,xhci,tablet
1st Boot

---
Defining the VM
framebuffer component
This (VNC) access method is insecure – use other means to get to your console over the internet (i.e. ssh tunnel).
This is non-accelerated graphics. No games or 3D!
1st Boot

---
What we have so far
bhyve \
      -H \
      -c 2 \
      -D \
      -l com1,/dev/nmdmfreebsd-vm0A \
      -l bootrom,/usr/local/share/uefi-firmware/BHYVE_UEFI.fd \
      -m 2G \
      -s 0,hostbridge \
      -s 1,ahci-cd,/lab/freebsd.iso \
      -s 2,nvme,/lab/freebsd-vm/disk.img \
      -s 3,lpc \
      -s 4,fbuf,tcp=127.0.0.1:5900,w=1600,h=900,password=secret,wait \
      -s 5,xhci,tablet \
      freebsd-vm
1st Boot

---
Basics of a VM
CPU
Memory
Firmware
Downloads
Host Bus / Bridge
Disk & Controller
Connectivity

---
Defining the VM
virtio-net component
tap – device node for user space interface
mac – specify MAC address
mtu
-s 5,virtio-net,tap0
Attach a Network Device

---
Defining the VM
bridge0
192.168.0.101
Attach a Network Device
tap0
ign0
vtnet0
em0
DHCP,
IP network
i.e. 192.168.0.0/24

---
Defining the VM
Routed vs Bridged Networking
How much do you trust your guests?
Do you want your guests to talk to each other directly?
Do you want to filter guest/guest traffic through a firewall (i.e. pf)?
Attach a Network Device

---
Defining the VM
bridge0
10.193.167.0/24
...
10.193.167.0/30
tapN
Other VMs
Attach a Network Device
tap0 10.193.167.1
NAT
DHCP,
IP network
i.e. 192.168.0.0/24
ign0
vtnet0
em0
192.168.0.101

---
Caveats
Routing requires forwarding enabled
gateway_enable=”YES”
sysctl net.inet.ip.forwarding=YES
Attach a Network Device

---
More caveats
tap goes through user space, alternatives exist but are more complex to configure
vale – virtual switch, not jails aware
netgraph – graph based, software defined networking
Adding a tap to a bridge: set IP address on your bridge, not on your tap!
Attach a Network Device

---
Tired of typing?
bhyve supports bhyve_config files
Provide the same input as program arguments
Saves you the typing
Easy to reuse
Easy to mistype and misconfigure
Recommendation: confirm your arguments are working, then convert
Attach a Network Device

---
Converting to config
bhyve <args> \
    -o config.dump=1 > config
All arguments end up in config, including -o.
Remove -o config.dump=1 before using the config file! Then run:
bhyve -k config
Attach a Network Device

---
Caveats: networking
Scripting your tap interface is more complex when left in config file – you can remove it and combine a config file with arguments:
bhyve -k config \
  -s 10,virtio-net,${TAP}
Attach a Network Device

---
ZFS Snapshot
Use ZFS to snapshot guest state
Only take snapshots while guest is off
Rollback only when guest is shut down
Allows transfer of guest data to another storage server and easy backup
Only put disk images on one single dataset if snapshotting all in the same state is desired
Hierachical datasets for recursive snapshots
ZFS Snapshots

---
UFS Snapshot
UFS supports snapshots too, however
Number of snapshots are limited
Performance degrades the more snapshots
They are not as convenient to use as with zfs
ZFS Snapshots

---
Using bhyveload
Allows preloading kernel from host filesystem
bhyveload loads kernel
bhyve starts afterwards and runs guest
bhyveload -m 2G -h / \
 -c /dev/nmdmfreebsd-vm0A \
 -e vfs.root.mountfrom=ufs:/dev/nda0p2 \
 freebsd-vm
ZFS Snapshots

---
Enhancing security
You can put bhyve in a jail! Attend the afternoon tutorial for an in-depth guide.
sysctl settings
jail.conf settings
devfs rules
ZFS Snapshots

---
Start on boot
There is no “standard” rc.script for bhyve
You can roll your own
Use daemon to wrap around bhyve
Define upfront: set up network before virtual machines or wrap around with cleanup?
You can use one of the existing management tools in ports
ZFS Snapshots

---
Management Tools
“You buried the lead!” …
actually, no: We now understand how things work “under the hood” and can fix things with more confidence
ZFS Snapshots

---
Weaknesses of tooling
Each tool follows its own paradigm
Single node operation
No guest introspection
No live migration (except where it does)
No snapshot/restore
Choose from “let me help you wrap your own” to the “kitchen sink” with exponential learning curve
ZFS Snapshots

---
A few choices
bmd
cbsd
vm-bhyve
vmstated
cirinna
There are even more and you might still have reasons for rolling your own!
Management Tools

---
bmd
Brainchild of Yuichiro Naito
Great integration with Mac OS
Very responsive developer
Powerful configuration language but very
intuitive pattern close to json and jails.conf
Lightweight daemon
Handles adding interfaces to bridges
No storage file handling
Ports version not up to date
bmd

---
bmd config
Config in /usr/local/etc/bmd.conf
bmdctl install -c <name>
bmdctl boot <name>
bmdctl console <name>
bmd

---
cbsd
Works with a multitude of hypervisors
Kitchen sink of hypervisor management
Steep learning curve
Very powerful, possibly intrusive
Includes concept for live migration
Full management solution
Pulls in many dependencies
Hard to uninstall
Russian origins
cbsd

---
vm-bhyve
Very complete solution
Guest and network/bridge management
Template based setup of guests
Storage handling
Easy to set up and learn
Shell based
Well established team of developers
vm-bhyve

---
vm-bhyve
Network setup
vm switch create -a 10.193.167.1/24 vmswitch
vm-bhyve

---
vm-bhyve
Shell based VM template language
loader="bhyveload"
cpu=1
memory=2G
network0_type="virtio-net"
network0_switch="vmswitch"
disk0_type="virtio-blk"
disk0_name="disk0"
disk0_dev="sparse-zvol"
vm-bhyve

---
cirinna
Go-Based
Only UEFI boot is supported, no bhyveload.
Relatively new
Handling similar to vm-bhyve
https://gitlab.com/swills/cirrina
vm-bhyve

---
vmstated
Follows base concept of “build your own”
Builds on bhyve_config files
Manages bhyve state only and allows hooking state changes
Your own hook scripts drive how the system behaves overall
Work in progress, slow development
Ports version finally catching up
vmstated

---
Performance I/O
Using a memory disk as backing storage
Non-volatile memory with all its risks
Good for performance tests
Pre-allocate memory for best results
Overcommit and kill your system!
mdconfig -o reserve -a -t malloc \
    -s 16G
Memory Disks

---
Virtualizing Windows
Wired memory required (-S)
UEFI only
nvme for storage
virtio-* requires drivers!
VNC/RDP is non-accelerated graphics!
PCI pass-through available for graphics and TPM but still a challenge to set up right
Windows and Linux

---
General Caveats
Hyperthreading and impact on virtualization
Going S2/S3 with a guest
Running on E-cores instead of P-cores
Pinning CPUs
Not fixing your MAC and ARP noise
BIOS settings and limiting performance
Sparse disk images and over-committing disk space
Use CPU yield (-H) to prevent hogging the CPU at 100% use

---
Cherry on top
Apache Guacamole for remote console
ssh into tmux sessions